## Slide 1
SMART AGRO ROVER
Autonomous Soil Monitoring & Navigation System
Final Year Engineering Project · 2026
Team Members
Member 1 · Member 2 · Member 3 · Member 4
Supervisor: [Supervisor Name]
🌱
Under $200
Budget
207
Tests Passing
12
Project Phases

## Slide 2
PRESENTATION OUTLINE
01
Problem Statement & Background
Africa farming challenge + motivation
02
Literature Review
5 papers · gaps identified · years cited
03
Research Gap & Objectives
What existing work misses · our targets
04
System Architecture
Dual-controller design rationale
05
Hardware Schematic & BOM
Components · connections · $195 budget
06
Sensor Suite
7 sensors · specifications · pin mapping
07
Software & Navigation
Firmware · mission logic · data pipeline
08
Simulation & Validation
Wokwi · Webots · 207 automated tests
09
Dashboard & Results
Flask UI · live monitoring · field data
10
Summary
Gap addressed · achievements · future work
2 / 12
Smart Agro Rover | 2026

## Slide 3
PROBLEM STATEMENT & BACKGROUND
African Agriculture Context
33M+
Smallholder farmers in
sub-Saharan Africa
70%
of Africa's food produced
by smallholder farmers
< 3%
use any form of precision
agriculture technology
40%
average crop loss due to
late disease detection
Ghana: cocoa, maize & yam farmers
rely entirely on manual monitoring.
The Problem
Crops inspected manually — slow, expensive, error-prone
Disease and drought detected only when visible damage occurs
Uniform irrigation applied regardless of actual soil conditions
No affordable automated monitoring tool for small farms
Our Solution
An autonomous 4WD rover that continuously surveys farmland, collects georeferenced soil and environmental data, detects obstacles, and delivers real-time insights through a web dashboard — all for under $200.
3 / 12
Smart Agro Rover | 2026

## Slide 4
LITERATURE REVIEW
Paper & Authors
Year
Key Contribution
Gap Identified
#
[1]
Kitić et al.
Agrobot Lala, MDPI Sensors
2022
Autonomous UGV, GPS waypoints, real-time nitrate soil analysis
~$20,000 cost. Requires wet chemistry lab. Not scalable to small farms.
[2]
NotBlackMagic
AutoSQA, Hackster.io
2023
Low-cost rover, BME688 sensor suite, autonomous field survey
Uses ROS 2 + expensive NXP NavQPlus. No offline mode.
[3]
Levoir et al.
RoboNav, MDPI Robotics
2022
u-blox GPS + IMU fusion, 0.2m waypoint accuracy in vineyard
Navigation only — no soil or environmental sensors integrated.
[4]
Hernanda et al.
MDPI AgriEngineering
2024
Dual-Arduino + Jetson Nano, GPS-RTK, IMU serial link at 10 Hz
Requires RTK-GPS ($500+) and ROS infrastructure. High cost.
[5]
Das et al.
PLOS ONE, BRAC Univ.
2024
4WD Pi rover + soil sensors + Pi Camera + YOLOv5 (85% precision)
Designed for vegetable harvesting only. No soil mapping or GPS nav.
AgroRover addresses ALL five gaps: under $200 · offline · full sensor suite · GPS navigation · no ROS required
4 / 12
Smart Agro Rover | 2026

## Slide 5
RESEARCH GAP & PROJECT OBJECTIVES
Identified Research Gaps
!
Cost barrier
Existing solutions cost $500–$20,000+. Inaccessible to smallholder farmers in developing nations.
!
ROS dependency
Most autonomous agri-robots require ROS, making them complex to deploy in the field.
!
No offline mode
Cloud-dependent systems fail in rural areas with poor connectivity.
!
Sensor + nav split
Papers either focus on navigation OR sensing — rarely both in one affordable system.
!
No African context
No reviewed solution was designed for West African farming conditions.
Project Objectives
1
Design
a sub-$200, dual-controller rover for autonomous soil monitoring
2
Implement
GPS waypoint navigation with obstacle avoidance
3
Integrate
7-sensor payload: moisture, temperature, humidity, pressure, ultrasonic, GPS, IMU
4
Develop
offline-capable data pipeline with Flask dashboard
5
Validate
complete system with 207 automated tests across all layers
5 / 12
Smart Agro Rover | 2026

## Slide 6
SYSTEM ARCHITECTURE — WHY TWO CONTROLLERS?
Gap addressed: Single MCU systems cannot simultaneously handle real-time sensor sampling AND complex navigation logic. Our dual-layer design solves this.
🧠 Raspberry Pi 4 — BRAIN
mission.py
Autonomous navigation logic
waypoint_nav.py
GPS boustrophedon survey
gps_reader.py
NEO-6M position + bearing
imu_reader.py
MPU-6050 heading / tilt
data_pipeline.py
CSV + SQLite data storage
app.py
Flask dashboard :5000
⇅
UART
Serial
JSON
115200
⚡ Arduino Nano — REFLEX
rover_firmware.ino
Real-time sensor sampling
Sensor hub
BME280 · DS18B20 · HC-SR04
Motor control
L298N PWM via D4/D5/D10/D12/D13
Encoder reading
LM393 × 4 wheels (D3·A2·A3·D11)
E-Stop logic
Hardware safety interrupt
JSON broadcast
Every 500ms to Pi
[1] Kitić et al. 2022 — Dual MCU+SBC architecture validated
[4] Hernanda et al. 2024 — Arduino + SBC serial at 10 Hz
6 / 12
Smart Agro Rover | 2026

## Slide 7
HARDWARE SCHEMATIC & BILL OF MATERIALS
LiPo 3S
11.1V
5200mAh
LM2596
Buck
11.1V→5V
Raspberry
Pi 4
Arduino
Nano
L298N
Motor Driver
4× DC
Motors
5V
UART
PWM
BME280
I²C A4/A5
DS18B20 ×2
1-Wire D2
Moisture ×2
Analog A0/A1
HC-SR04 ×2
D6/D7 D8/D9
GPS NEO-6M
UART Pi
MPU-6050
I²C Pi 0x68
Pi Camera v2
CSI Ribbon
LM393 Enc
D3·A2·A3·D11
Total BOM Cost: $195.40 · 27 components · Chassis: 4WD off-the-shelf · All components available in Ghana · Addresses cost gap [1][2][3][4]
7 / 12
Smart Agro Rover | 2026

## Slide 8
SENSOR SUITE — 7 SENSORS ADDRESSING GAP [3]
BME280
Air Temp · Humidity · Pressure
I²C 0x76 A4/A5 · ±0.5°C ±3%RH ±1hPa
DS18B20 #1
Soil Temperature Ch1
1-Wire D2 · −55 to +125°C ±0.5°C
DS18B20 #2
Soil Temperature Ch2
1-Wire D2 · Both on same bus
Cap. Moisture #1
Soil Moisture Ch1
Analog A0 · 0–100% capacitive
Cap. Moisture #2
Soil Moisture Ch2
Analog A1 · Corrosion-resistant
HC-SR04 Front
Obstacle Detection
TRIG D6 ECHO D7 · 2cm–400cm ±3mm
HC-SR04 Rear
Rear Clearance
TRIG D8 ECHO D9 · Prevents reversing into crops
GPS NEO-6M
Position + Bearing
UART /dev/ttyAMA0 · ±2m 9600 baud
MPU-6050
Heading · Pitch · Roll
I²C 0x68 Pi GPIO · ±250°/s ±2g
[3] Levoir et al. 2022 — GPS+IMU validated for field navigation · [5] Das et al. 2024 — Moisture+DS18B20 standard combination
8 / 12
Smart Agro Rover | 2026

## Slide 9
SOFTWARE ARCHITECTURE & NAVIGATION
Boustrophedon Survey
🤖
🏁 WP1
Crop rows →
Data & Mission Pipeline
1
Arduino samples sensors
Every 32ms — BME280, DS18B20, HC-SR04, Moisture
2
JSON broadcast to Pi
115200 baud · /dev/ttyUSB0 · 500ms interval
3
Pi parses + routes
serial_handler.py → sensor_hub.py — data stored
4
GPS + IMU navigation
waypoint_nav.py — Haversine bearing, boustrophedon
5
Obstacle check
us_front < 20cm → estop + avoidance manoeuvre
6
Data pipeline
data_pipeline.py → CSV + SQLite with lat/lon tag
7
Dashboard update
Flask app.py pushes live data to localhost:5000
[3] Levoir et al. 2022 — Haversine nav algorithm · [4] Hernanda et al. 2024 — Serial pipeline at 10 Hz
9 / 12
Smart Agro Rover | 2026

## Slide 10
SIMULATION & VALIDATION — 207 TESTS PASSING
⚡ Wokwi Simulation
Arduino Layer
Arduino Nano firmware in browser
DS18B20, BME280, HC-SR04 simulated
Potentiometers simulate soil moisture
Red/green LEDs for motor state
Push buttons: E-Stop + Reset
Serial Monitor: live JSON packets
58 Arduino unit tests passing
🌱 Webots Simulation
Full 3D Field
Clearpath Moose 4WD chassis
50m × 50m farm field with 5 crop rows
9 GPS waypoints, boustrophedon path
Cardboard box obstacles
GPS, IMU, Camera, 2× Ultrasonic
Console: live dashboard + JSON
75 Pi software tests passing
✅ Automated Test Suite
All Layers
58 Arduino firmware tests
75 Raspberry Pi software tests
74 integration tests
207 total — all passing
PC vision testing: 5 layers
Sensor test suite: 6 layers
Validate before physical build
10 / 12
Smart Agro Rover | 2026

## Slide 11
DASHBOARD & SYSTEM RESULTS
🌱 AGROROVER DASHBOARD · localhost:5000
SOIL MOISTURE CH1
68.4%
SOIL MOISTURE CH2
71.2%
SOIL TEMP CH1
24.3°C
AIR TEMPERATURE
28.7°C
HUMIDITY
64.2% RH
PRESSURE
1012.0 hPa
OBSTACLE DIST
382 cm ✅
GPS POSITION
5.6039°N 0.1875°W
HEADING
89.3° EAST
MISSION STATUS
SURVEY WP 3/9
System Performance
207
Tests Passing
$195
Total Cost
9
Waypoints Surveyed
(Webots sim)
7
Sensors Integrated
2Hz
Sensor Broadcast Rate
115200
Serial Baud Rate
11 / 12
Smart Agro Rover | 2026

## Slide 12
SUMMARY — CLOSING THE RESEARCH GAP
Problem: 33M+ African smallholder farmers lack affordable, autonomous soil monitoring — current solutions cost $500–$20,000+
✅ What We Achieved
Autonomous 4WD rover — under $200
GPS boustrophedon waypoint navigation
7-sensor payload (soil + air + vision + nav)
Dual-controller architecture (Pi + Arduino)
Offline Flask dashboard — no internet needed
207 automated tests — all passing
Wokwi + Webots simulation validated
Georeferenced soil data pipeline
⚡ Gaps Addressed [1][2][3][4][5]
→ Cost: $195 vs $500–$20,000 in literature
→ No ROS: pure Python on Raspberry Pi
→ Offline: SQLite + Flask, no cloud
→ Sensor + nav: both in one system
→ African context: small plot, low-cost
🔭 Future Work
→ Phase 10-12: Physical build + field trial
→ YOLOv5 crop disease detection [5]
→ Solar charging for extended runtime
→ ROS 2 migration for Nav2 stack
→ Multi-rover mesh network
12 / 12
Smart Agro Rover | 2026